## Slide 1: Assignment #2
OSPF Packet Capture

## Slide 2: Assignment #2 – OSPF Packet Capture
Purpose of this assignment
  Understanding OSPF router data structure
  Understanding OSPF Packet exchange flow
  Understanding how routing information database is synchronized among routers.
Submission (Due date is 2020/6/25)
  Report the OSPF router data structure and captured OSPF Packets based on the router data structure
    * Report must include sufficient explanation for packet contents and corresponding OSPF router structure
    * If you write value only without explanation on the report, you will get extremely low mark.
  Screen captures (the router data structure – use ospfd_mon)
  Captured packet file (Use wireshark save.)

## Slide 3: Example
  Example OSPF Router Data structure
  1. The router’s data structure shown by ospfd_mon

## Slide 4: Example
  Example OSPF Router Data structure
  2. You must explain why the data structure is like the above.
    It is the per-router data structure defined OSPF standard
    EXAMPLE: router id (first field)
      router ID value and definition (the 32-bit unique identifier of a router within the AS)
      We define the router id at the ospfd.conf configuration file as
        routerid 10.0.0.5.
      It is used at
        the router id field in the OSFP packet header
        neighbor id at “hello” packets’ neighbor list
        the advertising router id at the router-LSA
        the link state ID at the router-LSA
        the link ID field of the point-to-point link in the router LSA

## Slide 5: ospfd_mon commands
See the ospf_mon.jpg or ospf_mon>help
  areas
  interfaces
  neighbors
  database
  adv
  routes
  etc.

## Slide 6: ospfd_mon commands
adv <LS-Type> <Link State ID> <Advertising Rtr ID> <Area ID>
database <Area ID>

## Slide 7: Environment Setup
Network Topology
10.1.2.0/24
10.1.1.0/24
VM3
10.0.0.4
VM4
10.0.0.5
10.1.3.0/24
VM1
10.0.0.2
10.1.4.0/24
VM2
10.0.0.3
10.1.2.3
10.1.3.3
10.1.3.4
10.1.1.4
10.1.3.1
10.1.4.1
10.1.4.2
Subnet
Interface IP address
(VM Number)
(Router ID)
Router Name
and ID

## Slide 8: Environment Setup

## Slide 9: Environment Setup
Uncheck adapter(s) for inner network and check another adapter and select NAT

## Slide 10: Environment Setup
Place ospfd_com in ShareFolder
(shared folder on Windows)

## Slide 11: Environment Setup
Decompress ospfd_com.
Check whether ospfd and ospfd.conf is made both.

## Slide 12: Environment Setup

## Slide 13: Environment Setup
Click
1
2
Select one folder and one file, ospfd and ospfd.conf
Press Ctrl + C
3
Click

## Slide 14: Environment Setup
Ctrl + V

## Slide 15: Environment Setup
Make new folder

## Slide 16: Environment Setup
Folder name is ospfd_assignment
and Click Make
* Don’t change folder name!
Open folder and
Make folder again
Folder name : bin

## Slide 17: Environment Setup
Return to home
(Click Red box)

## Slide 18: Environment Setup
Folder name is httpd

## Slide 19: Environment Setup
Folder name is cgi-bin
Open folder and
Make new folder

## Slide 20: Environment Setup
Type "make install”

## Slide 21: Environment Setup

## Slide 22: Environment Setup
Change routerid
VM1 - 10.0.0.2
VM2 - 10.0.0.3
VM3 - 10.0.0.4
VM4 - 10.0.0.5

## Slide 23: Environment Setup
Set up
interface <IP address1> 10
ospfIfRtrPriority 10
ospfIfAuthType 0
interface <IP address2> 10
ospfIfRtrPriority 10
ospfIfAuthType 0
.
.
.
.
Type that as much as you have interface.

## Slide 24: Environment Setup
VM2
VM1
VM3

## Slide 25: Environment Setup
Repeat ppt 4~20 on each VM.
(Turn NAT on ~ edit ospfd.conf)

## Slide 26: Environment Setup
Turn VM1 off

## Slide 27: Environment Setup

## Slide 28: Environment Setup
1
2

## Slide 29: Environment Setup
Type VM4 as copied image file name
Click Next Next Next..

## Slide 30: Environment Setup
Click Next and Set up options such as RAM
to make new VM, VM4.

## Slide 31: Environment Setup
Input memory size you want

## Slide 32: Environment Setup

## Slide 33: Environment Setup

## Slide 34: Environment Setup
Click Make and Set up network setting of each VM. (also turn NAT off.)
10.1.2.0/24
10.1.1.0/24
VM3
10.0.0.4
VM4
10.0.0.5
10.1.3.0/24
VM1
10.0.0.2
10.1.4.0/24
VM2
10.0.0.3
10.1.2.3
10.1.3.3
10.1.3.4
10.1.1.4
10.1.3.1
10.1.4.1
10.1.4.2

## Slide 35: Environment Setup
Turn VMs on.
Edit /etc/network/interfaces on each VM and reboot VMs.
VM1
VM2

## Slide 36: Environment Setup
VM3
VM4
* Please don’t forgot to edit ospfd.conf of VM4

## Slide 37: Run wireshark and ospfd
On each VM, run wireshark and select “any“ (we should see packets for two interfaces at a same time.)

## Slide 38: Run wireshark and ospfd
ospf
Type ospf to use filter.

## Slide 39: Q & A
nampal02@korea.ac.kr
You can use assignment Q&A room of Collaborate by sending me an e-mail.